## Slide 1: NOAA Assessment of Unmanned Aircraft Systems for Hurricane Observations
Robbie Hood, Alexander MacDonald, Robert Atlas, Frank Marks, Steve Koch, Jim McFadden, Robert Rogers, Joseph Cione, Michael Black, Eric Uhlhorn, Christopher Landsea, Gary Wick, Paul Neiman, Nikki Prive, Scott Mackaro, Yuanfu Xie, Phil Hall, Nancy Ash, and Phil Eastman

## Slide 2: Overview of NOAA UAS Program
The NOAA Unmanned Aircraft Systems (UAS) Program is evaluating the feasibility of UAS platforms to meet the NOAA Mission’s goals in
    Climate
    Weather and Water
    Ecosystems
    Commerce and Transportation
using a requirements-driven systems approach to assess technology readiness and operational feasibility

## Slide 3: Assessing UAS Technologies
Field Demonstrations and Flight Testing
Observing System Simulation Experiments (OSSE) and Observing System Experiments (OSE)
System Analysis of Technology Readiness:
  Current Platforms,
  Payloads,
  Observing Strategies
  Information Management
  Applications
  Data Assimilation

## Slide 4: Low Altitude Long Endurance (LALE) Unmanned Aircraft Systems (UAS)
LALE Field Testing
Led by Joe Cione (HRD) and Nancy Ash (AOC)
2005 – Hurricane Ophelia
2007 – Hurricane Noel
Hurricane Ophelia Imagery
Hurricane Noel Wind Data

## Slide 5: NASA Genesis Rapid Intensification Processes (GRIP) Experiment
Global Hawk dropsonde development in collaboration with NSF and NCAR
Hurricane Imaging Radiometer development in collaboration with NASA
NASA Global Hawk Missions
NASA WB-7 Missions
Ocean Wind Speed
Ocean Rainfall
Sea Surface Temperature

## Slide 6: Expendable Platforms
Airspeed: 60 kts cruise, 85 kts dash
Deployment Altitude: up to 20,000 ft MSL
Operational Altitude: 500-2,000 ft AGL
Range: 20nm LOS (extending to 50nm)
Endurance: 1 hr @ cruise (extending to 1.5 hrs)
COYOTE UAS
Low Altitude Balloons in partnership with WISDOM

## Slide 7: Observing System Simulation Experiment (OSSE)
An OSSE is a modeling experiment used to evaluate the impact of new observing systems on operational forecasts when actual observational data are not available
UAS OSSE will be used to guide acquisition, flight planning, sensor development decisions
Current efforts include global weather OSSE and regional hurricane OSSE

## Slide 8: UAS Technology Readiness Level (TRL) Assessment
TRL DEFINITION
Basic principles observed and reported
Technology concept and/or applications formulated
Analytical and experimental critical function and/or characteristics
Component and/or breadboard validation in laboratory environment
Component and/or breadboard validation in relevant environment
System/subsystem model or prototyping demonstration in a relevant environment (ground or air)
System prototyping demonstration in a flight environment
Actual system completed and “flight qualified” through test and demonstration (ground or air)
Actual system “flight proven” through successful mission operations

## Slide 9: Dropsonde Technology Assessment
FY10
FY11
  Sondes from low altitude – TRL 9
  Sondes from medium altitude – TRL 9
  Sondes from high altitude – TRL 7 (system prototype in flight environment)
  MIST sondes – TRL 5 (component in relevant environment)
  MIST sondes from Global Hawk – TRL 5 (components in relevant environment)
  MIST sondes from Global Hawk – TRL 6 (system in relevant environment)
  OR
  MIST sondes from Global Hawk – TRL 7 (system in flight environment)
  Depending on the science objective for hurricanes, atmospheric rivers, or winter storms

## Slide 10: Low Altitude UAS Technology Assessment
FY10
FY11
  Aerosonde platform in hurricane – TRL5 (component in relevant environment)
  Aerosonde payload in hurricane – TRL 4/5 depending on sensor ( components in laboratory/relevant environment)
  Manta platform in atmospheric rivers – TRL 5 (component in relevant environment)
  Manta platform in atmospheric rivers – TRL 4/5 ( components in laboratory/relevant environment)
  Coyote platform from P-3 – TRL 5 (Component in relevant environment)
  Manta platform and payload in atmospheric rivers – FY 6 (system prototype in relevant environment)
  Coyote platform and payload in hurricanes – TRL 6 (system in relevant environment)
  OR
  Coyote platform and payload in hurricanes – TRL 7 (system in flight environment)

## Slide 11
00Z 9-15
00Z 9-16
00Z 9-17
00Z 9-18
00Z 9-19
GV
08Z
18Z
14Z
18Z
GH
10Z
18Z
DC8
P3-43
P3-43
P3-43
P3-42
P3-42
P3-42
20Z
05Z
20Z
00Z
20Z
05Z
08Z
17Z
08Z
12Z
08Z
17Z
GRIP Dry Run All Aircraft Schedule
15-19 September 2009
Version: 16Sep09
Tuesday
Wednesday
Thursday
Friday
08Z
18Z
GV
Bahamas
Bahamas
ex-Fred
08Z
18Z
GV
ex-Fred
Bahamas
Bahamas
Bahamas
ex-Fred
ex-Fred
ferry
ferry
10Z
18Z
DC8
ex-Fred
18Z
00Z
GH
PG24
P3-43
20Z
05Z
ex-Fred tbd
Flight decision made at 19Z

## Slide 12: Examples of Dropsonde Coverage
NASA DC-8 flight Hurricane Erin 2001
NASA Global Hawk dry run exercise for Extratropical Fred 2009
NOAA G-IV flight for Hurricane Bill 2009

## Slide 13: Contact Information
NOAA UAS Web Site
http://UAS.noaa.gov
NOAA UAS Program Director
Robbie.Hood@noaa.gov
301-734-1102 (office)
303-905-3411 (cell)

## Slide 14
MTP
Payloads from NASA GloPac Campaign